## Slide 1: Deployment Modes

## Slide 2: Top 7 E-Class & SuperMassive Deployments
Traditional NAT Gateway with Security & Remote Access
In-Line Deployments: Wire mode or Layer 2 Bridge Mode, Tap Mode
  Easy Network Insertion, no network re-numbering
High Availability Modes
  Active/Passive with State Synchronization
  Active/Active DPI with State Synchronization
  Active/Active Clustering
“Clean Wireless” Deployment
  Firewall as a wireless controller
  DPI on all wireless traffic
“CleanVPN” Deployment
  Firewall as a VPN Concentrator
  DPI on all incoming VPN traffic
VPN Concentrator for Distributed Enterprise
  Global Management System (GMS) to provision and manage branch offices
  Connectivity through central SuperMassive or E-Class NSA firewall
  All security done at the central site
Network Segmentation (Security Zones)
  Network Segmentation via VLAN & Security Zones
  Different Security policies for each Security Zone

## Slide 3: Distributed Enterprise with CleanVPN and GMS Management
Branch Office
Branch Office
Remote Home Office
Head office
Major Campus
Data Center
Data Center
Secure and Efficient Distributed Enterprise with Dell SonicWALL Firewalls for all Network Locations
“Clean VPN”
TZ 215
NSA 220
TZ 205
NSA E8510
NSA E8510
NSA E6500
E10800
Global Management System

## Slide 4: High Availability

## Slide 5: General Concepts
Use redundancy to minimize downtime in event of hardware or firmware failure
Firewalls in HA Pair operate in Active/Standby mode
  Only Active firewall is forwarding traffic
  Standby firewall is waiting to take over if Active firewalls fails
Primary and Secondary firewalls “share” interface IP addresses
  Only Static IP addresses are supported for WAN interfaces

## Slide 6: Terminology and Setup
Primary SonicWALL
Secondary SonicWALL
WAN
LAN
WAN
LAN
HA
Currently active system
Currently Standby system
Currently active system
Currently Standby system
Notes: 6
6
In the case when the Primary unit experiences a failure, the Backup hardware will take over. When the Primary becomes available again, it will remain in an Standby state and the Backup will remain in an active state. If preempt mode is configured, then the Primary unit will reassume its role as active and the Backup will return to Standby.

## Slide 7: Virtual IP Address
WAN
LAN
Shared “virtual” IP or VIP
All network traffic uses the shared IP
WAN
LAN
.1
.1
.2
.2
.3
.3
LAN VIP
WAN VIP
Shared IP Address On Each Interface Pair
Notes: 7
VIP
Primary Management IP
Backup Management IP

## Slide 8: HA Management IPs
Primary
Secondary
Virtual IP is required in all circumstances
Two HA management IPs are required for LAN, but are optional for WAN
Although you do not need three addresses on the WAN side, we recommend using three addresses on WAN interfaces (if you have them) to give greater management flexibility
WAN
LAN
WAN
LAN
HA
.1
.1
.2
.2
.3
.3
WAN Virtual IP
Notes: 8
Management IP enables the administrator to access each HA unit whether it is in an active or idle state. If the VIP is used for access then the administrator will always be sent to the active unit, whether it is the Primary or Backup unit.
The management IP address of the Secondary/Idle unit is used to allow license synchronization with the SonicWALL licensing server, which handles licensing on a per-appliance basis (not per-HA Pair). Even if the Secondary unit was already registered on MySonicWALL before creating the HA association, you must use the link on the System > Licenses page to connect to the SonicWALL server while accessing the Secondary appliance through its management IP address.

## Slide 9: HA Control Link
Active and Standby Firewalls communicate over HA Control Link
Heartbeat packets are exchanged between Active and Standby
  Heartbeat includes HA State, Serial Number, Hardware Info, Physical link state, preferences (settings) timestamp
Preferences and firmware are also synced over HA Control Link
Highly recommend that HA Control link is a direct cross-connect cable between Primary and Secondary.
Can use a Layer-2 switch in some cases.
  Be sure switch can forwards custom Ethernet type traffic.
  Using a Layer-2 switch adds another point of failure
HA units in different geographic locations
  Make sure latency is low (below half of heartbeat interval)

## Slide 10: HA Control Link Failure
If HA Control Link fails, heartbeat packets sent over X0 interface
Failover still supported.
  Based on information exchanged in heartbeats.
No preferences or firmware sync.
  If needed, full preferences sync performed when HA-link comes back up.

## Slide 11: Preferences
Firewall configuration settings are commonly referred to as Preferences or prefs
Settings automatically synced from Active to Standby firewall over HA Control Link.
  Administrator can log in to Standby firewall
  Standby firewall is in read-only mode.
Incremental sync
  Done when preferences on Standby already in sync.
Full preferences sync
  Done when preferences on Standby are old.
  Standby reboots itself afterwards (to load new preferences).

## Slide 12: Firmware Upgrade
Two step process – upload and boot
Upload
  Active unit downloads new firmware
  Active unit sends new firmware to Standby unit via HA Control Link
Boot
  Standby unit reboots first
  Standby unit takes over as Active after reboot
  Previously Active unit reboots second
  Active/Standby roles are reversed after a reboot

## Slide 13: Pre-emption
‘Preempt’ mode used to ensure that when possible, Primary firewall is Active
Primary firewall must have link state equivalent to Secondary before it can be pre-empted
Firmware upgrade results in an additional reboot cycle
Not recommended unless there is definitive need

## Slide 14: HA Failover
Time to failover depends on the type of failure.
  Monitored physical link failure
    Standby learns of failure from heartbeat from peer.
    Standby will only failover if it has better link state.
    Failover almost instantaneous.
  Logical link failure
    Only happens after configured number of probes lost.
    Standby learns of failure from heartbeat from peer
    Standby will only failover if it has better link state.
    Failover takes (probe-interval X failed-probe) seconds.

## Slide 15: This Table Governs Behavior During Link Failures
Active Unit Ping Status | Standby Unit Ping Status | Result
 |  | No change; Ref. is broken
 |  | No change
 |  | Active Unit stays active
 |  | Standby Unit becomes active
Notes: 15
15

## Slide 16: HA Failover
Time to failover depends on the type of failure:
  Active firewall restarted by Admin
    Standby learns of pending reboot from heartbeat.
    Failover almost instantaneous.
  Active firewall detects firmware failure
    Standby learns of Active firmware failure from heartbeat.
    Failover almost instantaneous.
  Active firewall looses power
    Only happens after configured number of heartbeats missed.
    Failover takes (heartbeat-interval X missed-heartbeats) milliseconds.

## Slide 17: HA Failover
Standby failover takes over from Active by announcing itself on the network.
  Sends Gratuitous ARPs for all VIPs and other IP addresses it is taking over from the failed Active.
  Allows all connected Layer-2 devices to learn of new ‘location’ and MAC address for IP addresses.

## Slide 18: Virtual MAC
Active and Standby unit can also share common Layer-2 MAC address.
  Virtual MAC ‘generated’ from MAC address of interface on Primary.
  Interface virtual MAC can be specified by Admin.
When Virtual MAC used, it looks like the firewall has ‘moved’ on the network.
Highly recommended
  Seamless traffic failover
  Only the connected L2 devices (Switches) need to learn of Virtual MAC move
If Virtual MAC is not used
  Traffic failover time is dependent on behavior of connected L3 devices (Routers)
  ARP needs to be re-learned on connected L3 devices for traffic to failover

## Slide 19: Virtual MAC
00 | 17 | C5 | 19 | E1 | 40
02 | 17 | C5 | 19 | E1 | 40
OUI
Physical MAC Address (Primary)
Virtual Mac Address
L
M
b1
b7
b8
L = IEEE 802.3 ‘local’ bit

## Slide 20: Basic High Availability
Provides most basic failover support
Standby firewall does not maintain any state (other than preferences)
  It is a ‘cold’ standby
Upon failover, all existing connections no longer valid
  Hosts need to re-initiate connection

## Slide 21: Stateful High Availability
Built on top of Basic High Availability.
In addition to preferences, Application state information synced in real-time.
  Standby firewall is now a ‘hot’ standby.
As most real-time state information synced, failover is transparent to hosts.
  Established connections can continue after failover
Application state information synced over HA Data Link.

## Slide 22: Stateful Failover
LAN
WAN
LAN
WAN
traffic
traffic
HA
HA
Sync info
Active
Standby
Active
Notes: 22
22
Stateful failover add supports for the Idle firewall to be a ‘hot’ standby. Specific protocol/application state information is synced so that upon failover existing connections can continue to be used. The failover is transparent!

## Slide 23: Stateful Failover
‘Application’ state information synced
  Simple Connections
    Telnet, HTTP, Ping, etc.
  Related Connections
    FTP, Oracle SQL-NET, Real Audio, RTSP
  DHCP Server Lease information
  VPN
    Tunnels, GVC information
  ARP Table
  Dynamic Address Objects (FQDN AO, MAC AO)
  Active Users.
  Multicast/IGMP

## Slide 24: Stateful Failover
Application’ state information synced
  Wireless
    Sonicpoint, Wireless Guest Status
  WAN Load Balancing state
  Routing
    RIP and OSPF

## Slide 25: Stateful Failover
Application state information not synced
  VoIP
    SIP, H.323
  PPP clients
  L2TP Server
  Security Services
    GAV, IPS, Anti Spyware, CFS
  SYN Flood protection state
No state-sync across a firmware upgrade.

## Slide 26: HA Licensing
Handled through MySonicwall.com
Security Services licenses are “shared’ between two devices, so only have to buy one set
  MySonicwall.com needs to know that two devices are bound together to build the HA Keys
HA Monitoring IP addresses of the Standby unit are used for license synchronization and signature downloads
Notes: 26

## Slide 27: Shared Licensing
Global VPN Client
Global VPN Client Enterprise
Server Anti-Virus
Stateful High Availability Upgrade
Comprehensive Anti-Spam
Client/Server Anti-Virus Suite
Comprehensive Gateway Security Suite
Content Filtering: Premium Edition
Content Filtering: Standard Edition
Enforced Client Anti-Virus and Anti-Spyware
IPS
Gateway Anti-Virus
Anti-Spyware

## Slide 28: Individual Licensing
Support is not shared between units in HA-pair
  Dynamic Support 24x7
  Dynamic Support 8x5
Each unit must have Support licensed individually.

## Slide 29: HA Interfaces
GEN5
  Fixed interface for HA
  E-Class devices have dedicated HA port
  For non E-Class devices last physical port automatically chosen as the HA port
  No separate interface for State-sync
GEN6
  Configurable interfaces for HA ("HA control" interface)
  Separate interface possible for State-sync (“HA Data” interface)
  HA Data interface can overlap with HA Control
  Interface recommendations (not restrictions)
    1 G for HA control
    1G-10 G for HA Data (depending on the device)

## Slide 30: HA Interfaces
Supermassive 10X00
  Configurable interfaces for HA ("HA Control" interface)
  Separate interface required for State-sync (“HA Data” Interface)
  HA Data interface CANNOT overlap with HA Control
  Interface recommendations
    1 G for HA control (restricted)
    10 G for State-sync (1 G is also allowed if needed)
  6.0.5 release has dedicated HA backup port feature (currently under QA)

## Slide 31: Active/Active DPI

## Slide 32: Active/Active DPI
Works on top of Stateful HA, internally firewalls are Active/Standby with Stateful sync enabled
  Requires an additional interface (“Active/Active DPI Interface”) to be configured to interconnect HA units
  On SM10000 series restricted to be a 10G interfaces
Traffic for select connections off-loaded by Active firewall to Standby firewall for Security Service processing.
Standby firewall receives the traffic packets over the Active/Active DPI Interface

## Slide 33: Active/Active DPI
Packets enter and leave via Active firewall
Some traffic is offloaded to Standby firewall for DPI processing
Once received, Standby firewall does DPI processing and returns the packets back over the Active/Active DPI Interface.
Standby firewall is used for computational intensive processing only.
  Standby firewall does NOT forward the data traffic
On Gen5, optionally an additional interface (“AA DPI Interface2”) can be configured for load sharing AADPI traffic

## Slide 34: Active/Active Clustering

## Slide 35: Active/Active Clustering Basics
AA Cluster is formed by a collection of 2 or more Cluster Nodes
Each Cluster Node is a Stateful HA pair with Primary & Secondary devices
Upto 4 Cluster Nodes supported
  On Gen6/SM10000 series, additional interfaces (“AA Cluster Links”) need to be configured for cluster communication
  Restricted to be 1 G interfaces

## Slide 36: Active/Active Clustering Basics
SVRRP (SonicWALL VRRP) protocols is used for communicating between Cluster Nodes
HA & Stateful HA protocols are used for communicating within a Cluster Node
Each Cluster Node actively processes traffic in parallel
Load Balancing traffic between Cluster Nodes is handled outside the firewall

## Slide 37: Active/Active Clustering – 2 Node Topology (Gen5)

## Slide 38: Active/Active Clustering – 2 Node Topology (Gen6)

## Slide 39: Virtual Group
Firewall configuration is divided by Virtual Groups
Virtual Group is
  Collection of Interface IP addresses
  NAT Policies
  VPN Policies
  ….
A Cluster Node can own 1 or more Virtual Groups
  Cluster Node processes traffic for Virtual Group it owns
  Ownership of Virtual Group is determined by configuration
  Typically each Cluster Node owns one Virtual Group
Number of Virtual Groups is equal to number of Cluster Nodes

## Slide 40: Active/Active Clustering Sync
Configuration is synced across all Cluster Nodes
Dynamic State is NOT synced across all Cluster Nodes
Owner of Virtual Group is designated as Master Node
Configuration is done via Master Node
Master Node is responsible for syncing configuration/firmware to all Cluster Nodes

## Slide 41: Active/Active Clustering - Benefits
Higher throughput
Higher number of Connections
Higher Connection setup rate
No single point of failure
Scalable design

## Slide 42: High Availability New Features

## Slide 43: HA Features (under development)
State Sync support during Firmware upgrade
Use of LAG / Redundant ports for HA Control / HA Data / AA DPI Links
Active/Active
  State Sync between Active Firewalls
  L2/L3 Load Balancing between Active Firewalls (under investigation)
HA support for Multi-Tenancy

## Slide 44: Deployment Scenarios

## Slide 45: Deployment scenarios
Active / Passive
Active / Passive with Stateful Sync
Active / Active DPI
Active / Active Clustering
Firewall Sandwich

## Slide 46: Active / Passive
One Active passing traffic, One Idle
HA Links:
  HA Control, configurable
  HA Backup X0 (1)
(1) On SuperMassive 9K 6.0.5.x configurable
X0
X0
HA
Heartbeat + Settings Synchronisation
Heartbeat
Active
Idle

## Slide 47: Active / Passive, Idle Unit Signature Download
One Active passing traffic, One Idle
HA Links:
  HA Control, configurable
  HA Backup X0
Management Addresses on X0 required, always connect X0
X0
X0
HA
Heartbeat + Settings Synchronisation
Heartbeat + Signature Download
Active
Idle

## Slide 48: Active / Passive, X0
Using X0 Parent as HA Backup
Unique VLAN purely for HA Backup
Still advised to AVOID mixing Tagged and Untagged traffic
X0
X0
HA
Active
Idle
U V100
T V10
U V100
T V10
T V100
T V10

## Slide 49: Active / Passive
One Active passing traffic, One Idle
HA Links:
  HA Control, configurable
  HA Backup X0
Management Addresses on X0 required (1)
Virtual MAC strongly advised (1)
(1) Applicable for all setups with an Active/Idle Pair
X0
X0
HA
Heartbeat + Settings Synchronisation
Heartbeat + Signature Download
Active
Idle

## Slide 50: Active / Passive – Virtual MAC (VMAC)
Virtual MAC?
Without Virtual MAC, active unit uses own MAC
On Failover GRATUTIOUS ARP sent
Older Network equipment does not accept Grat Arps, use VMAC
MAC – IP Spoof protection will prevent MAC – IP changes, use VMAC
ARP Cache timeout generally 2 minutes
Switch Security mechanism prevent MAC – Port change, no VMAC
X0
X0
HA
Active
Idle

## Slide 51: Active / Passive with Stateful Sync
One Active passing traffic, One Idle
HA Links:
  HA Control, configurable
  HA Data, configurable
  HA Backup X0
HA Control and HA Data CAN be the same interface (1)
(1) SM 10K excepted
X0
X0
HA
Heartbeat + Settings Synchronisation
Session Sync
Heartbeat
Active
Idle
HA Data
HA Control

## Slide 52: Active / Passive with Stateful Sync - Data Link
Dedicated HA Data Link?
Dependent on Session data needed to be synced
When using 10 Gbps links always use a dedicated HA Data Link
X0
X0
Active
Idle
HA Data
HA Control

## Slide 53: Active / Passive with Stateful Sync
One Active passing traffic, One Idle
HA Links:
  HA Control, configurable
  HA Data, configurable
  HA Backup X0
Management Addresses on X0 required
Virtual MAC strongly advised
X0
X0
Heartbeat + Settings Synchronisation
Session Sync
Heartbeat
Active
Idle
HA Data
HA Control

## Slide 54: Active / Active DPI
One Active passing traffic, One Idle
HA Links:
  HA Control, configurable
  HA Data, configurable
  HA Data 2, Configurable
  HA Backup X0
HA Control and HA Data CAN be the same interface (1)
(1) SM 10K excepted
X0
X0
HA
Heartbeat + Settings Synchronisation
Session Sync
DPI Ofloading
Heartbeat
Active
Idle
HA Data
HA Control
40 – 60 %
aka DPI Ofloading

## Slide 55: Active / Active DPI – Data Link 1 or 10 Gbps
HA Data 2, 1 Gbps or 10 Gbps?
Advised to use a 10 Gbps
X0
X0
Active
Idle
HA Data
HA Control

## Slide 56: Active / Active DPI
One Active passing traffic, One Idle
HA Links:
  HA Control, configurable
  HA Data, configurable
  HA Data 2, Configurable
  HA Backup X0
Management Addresses on X0 required
Virtual MAC strongly advised
X0
X0
Heartbeat + Settings Synchronisation
Session Sync
DPI Ofloading
Heartbeat
Active
Idle
HA Data
HA Control
40 – 60 %

## Slide 57: Active / Active Cluster
Two or more Active nodes
Currently support 4 Nodes
A node is either a Standalone Unit or an Active/Idle pair (1)
HA Links:
  Clusterlink 1, configurable
  Clusterlink 2, configurable
(1) UI currently requires Backup Serials to be defined, use fake serials.
X0
X0
HA
Heartbeat + Settings Synchronisation
Heartbeat + Settings Synchronisation
Active
Active
Node1
Node2
Between Nodes
Cluster

## Slide 58: Active / Active Cluster – A/I HA Pair
Standalone unit or A/I HA Pair as a node?
Failover between Nodes is STATELESS
X0
X0
Active
Active
Node1
Node2
Cluster

## Slide 59: Active/Active cluster – Standard operation
VG = Virtual IP Group = Collection of Interface IP addresses (e.g X0,X1,X2 etc)

## Slide 60: Active/Active clustering – Unit failure

## Slide 61: Active/Active cluster – Two-unit failover

## Slide 62: Active/Active cluster – Node failure

## Slide 63: Active/Active cluster – Node restored

## Slide 64: Active / Active Cluster – Caveats
Failover between Nodes is STATELESS
Need intelligence inside the network for LoadBalancing Traffic
ALL Units must be connected to ALL Networks
NO SESSION SYNC BETWEEN NODES
X0
X0
Active
Active
Node1
Node2
Cluster

## Slide 65: Active / Active Cluster – Asynchronous Routing
NO SESSION SYNC BETWEEN NODES
X0
X0
Active
Active
Node1
Node2
Cluster
X2
X2
VLAN 10
DG=X0 VG1
VLAN 20
DG=X2 VG2

## Slide 66: Active / Active Cluster – When Usable
Single LAN – WAN (MultiWAN) setup
DR Site
X0
X0
Active
Active
Node1
Node2
Cluster

## Slide 67
 | A/P HA | Stateful HA | A/A DPI | A/A Clustering* | BGP
TZ SOHO | N/A | N/A | N/A | N/A | N/A
TZ 300 | Yes but no special price on HA unit | N/A | N/A | N/A | N/A
TZ 400 | Yes but no special price on HA unit | N/A | N/A | N/A | Expanded (01-SSC-0573)
TZ 500 | HA Unit (01-SSC-0439) | Stateful HA (01-SSC-0494) or Expanded (01-SSC-0502) | N/A | N/A | Expanded (01-SSC-0502)
TZ 600 | HA Unit (01-SSC-0220) | Stateful HA (01-SSC-0264) or Expanded (01-SSC-0266) | N/A | N/A | Expanded (01-SSC-0266)
NSA 2600 | HA Unit (01-SSC-3861) | Stateful HA (01-SSC-7095) or Expanded (01-SSC-7090) | N/A | N/A | Expanded (01-SSC-7090)
NSA 3600 | HA Unit (01-SSC-3851) | Stateful HA (01-SSC-7094) or Expanded (01-SSC-7091) | N/A | N/A | Expanded (01-SSC-7091)
NSA 4600 | HA Unit (01-SSC-3841) | Included | N/A | N/A | Included
NSA 5600 | HA Unit (01-SSC-3831) | Included | Expanded (01-SSC-4480) | Expanded (01-SSC-4480) | Included
NSA 6600 | HA Unit (01-SSC-3821) | Included | Expanded (01-SSC-4481) | Expanded (01-SSC-4481) | Included
SM 9200 | HA Unit (01-SSC-3811) | Included | Included | Included | Included
SM 9400 | HA Unit (01-SSC-3801) | Included | Included | Included | Included
SM 9600 | HA Unit (01-SSC-3881) | Included | Included | Included | Included
SM 9800 | HA Unit (01-SSC-0801) | Included | Included | Included | Included
* A/A Clustering required minimum 2 unit (full price, no HA unit) + licenses for each unit
HA A/A DPI additional and expanded licenses BGP

## Slide 68
Dell SonicWALL FireWALL Sandwich

## Slide 69: Firewall Sandwich

## Slide 70: What is a FireWALL Sandwich (FWS)?
“A scale-out, highly resilient Layer 2 architecture providing transparent security services to enhance existing security solutions, separate security functions or provide added capacity”
DOES NOT:
  Provide Layer 3 services (routing, NAT)
  Replace traditional HA firewall architectures
  Address the needs of typical small/medium customers
DOES:
  Work with Dell Networking S4810, S5000 and Dell Network Security SuperMassive 9x00 series products
  Scale to 144Gbps of DPI, 320Gbps of SPI , 256,000 SSL-DPI sessions and 40m connections
  Provide N+1 redundancy (vs. 1+1) without reliance on HA or clustering protocols
  Support 1, 10 or 40GE ingress/egress connections (today) and performance
  Allow compete with Juniper, Cisco, Fortinet, Palo Alto and Check Point at the high-end with better TCO

## Slide 71: Why such a design?
Networking reasons
  Scalability, commoditization of 10/40 GbE
  Convergence of layers
  Redundancy and resiliency
  Increases in east to west traffic
    Virtualization, Datacenters
Security reasons
  Scalability, commoditization of 10/40 GbE
  Inspection at the Distribution/Core layer not just Access Layer (Perimiter)
  East to West inspection
  Malware Lifecycle (lateral movements, exfiltration, reconnaissance)

## Slide 72: FWS Architecture
Blueprint for deploying a network-based scale-out security layer architecture
Highly resilient Layer 2 design offering transparent security services to enhance existing security solutions, separate security functions or provide added capacity”
Fully validate with Dell Networking S4810, S5000, S6000 and Dell Network Security SuperMassive 9x00 series NGFW products
Provide N+1 redundancy (vs. 1+1) without reliance on HA or clustering protocols
Support 1, 10 or 40GE ingress/egress connections (today) and performance
Technologies utilized: VLT, Symmetric Hashing, Port Channel LAG, Active Mesh

## Slide 73: FWS Architecture with S5000 and SM 9K
4 x S5000 switches
  1/10/40GE connections
  Load-balance IP SA/DA flows
  Stacked/VLT
  Primary and Bypass LAG
N x SM9x00 firewalls
  10GE connections
  Wire Mode
  Security Services
  No HA or Clustering
  Stateful Inspection Disabled

## Slide 74: FWS Configuration
S5000 ingress/egress switch layer
  Configure stacking for ingress/egress pairs
    Use 40GE interfaces for stack backplane
  Configure primary port-channel using LACP
    Add 10GE interfaces for firewall connections
    Set as switchport (Layer 2)
    Define backup port-channel and min links
  Configure backup port-channel using LACP
    Use 40GE interfaces for bypass LAG
    Set as switchport (Layer 2)
  Configure ingress/egress interfaces
    Add VLANs as required and assign to port-channels
    Set as switchport (Layer 2)
  Configure Load-balancing
    Set hashing algorithm and seed value
    Set load-balancing method
SuperMassive 9x00 security layer
  Configure WAN interface for management and register/license
    Set DNS, NTP, update signatures, etc
  Configure ingress/egress Wire Mode pair
    Configure zones
    Configure Protect Wire Mode
    Disable Stateful Inspection
  Configure security services
    App Control, CFS, IPS, GAV, Anti-Spyware, Geo-IP, Botnet Filter and DPI-SSL are supported
  Enable security services for zone(s)
    Configure desired firewall policies
  Configure management and reporting
    Syslog, IPFIX Extended (Splunk)

## Slide 75: Firewall Sandwich Types:
Classic Firewall Sandwich
The Double Firewall Sandwich
The Open Firewall Sandwich

## Slide 76: Firewall sandwich deployment options for all customer scenarios : The Classic Firewall Sandwich
Customer currently owns and opts to keep their existing firewall infrastructure
  Usually a Cisco or Juniper solution deployed at the perimeter for Stateful Packet Inspection, Routing, and NAT
  Would like to add Deep Packet Inspection : Cisco and Juniper are unable to provide this at an effective price point
  Non-intrusive deployment, highly resilient design
Perimeter
Distribution
Routing/Stateful
Deep Packet
Inspection

## Slide 77: Firewall sandwich deployment options for all customer scenarios : The Double Firewall Sandwich
Customer would like to completely replace their existing firewall infrastructure and go all Dell!
  Requires Routing and Deep Packet Inspection solutions
  While maintaining high performance and superb resiliency
  Dell-SonicWALL NGFW High Availability Pair, at the perimeter providing Layer 3 services
  Classic Firewall Sandwich, providing all Deep Packet Inspection Services
Perimeter
Distribution
Routing/Stateful
Deep Packet
Inspection

## Slide 78: Firewall sandwich deployment options for all customer scenarios : The Open Firewall Sandwich
  Customer would like to replace their firewall solution with Dell-SonicWALL’s but would prefer to leverage their existing switch infrastructure
  Requires enormous amount of NAT and concurrent connections
  3rd party Layer 3 Network Loadbalancer needed
Perimeter
Routing/Stateful
Deep Packet Inspection
Link Aggregation
Loadbalancer
Loadbalancer
Distribution
Internet
or
L3 Load balancer

## Slide 79: How far does it scale?
Cluster of Firewall Blades configuration (Wiremode. NATed, Routed) |  |  |  |  |  |  | 
Firewall Mode | Security Services | Platform | Dell F10 Switches | Throughput | DPI-SSL Throughput | TCP connection per seconds | Max Concurrent TCP connections
Wiremode | IPS+ App Intelligence | SM9400 (16 units) | S5000, S6000 | 160G (120G recommended for redundancy) | 40G | 2.2 Million | 24 Million
 | IPS+ App Intelligence | SM9800 (16 units) | S5000, S6000 | 320G (240G recommended for redundancy) | 80G | 4.5 Million | 40 Million
 | IPS, GAV, ASPY and Application Intelligence | SM9800 (16 units) | S5000, S6000 | 160G (120G recommended for redundancy) | 80G | 4.5 Million | 40 Million
NATed/Routed | IPS, GAV, ASPY and Application Intelligence | SM9400 (16 units) + 4 X SM9800 | S5000, S6000 | 120G | 40G | 1.1 Million | 12 Million
 | IPS, GAV, ASPY and Application Intelligence | SM9800 (16 units) + 4 X SM10800 | S5000, S6000 | 120G | 80G | 1.6 Million | 40 Million

## Slide 80
What’s in the Demo?
Demo Rack
Turn on the heat and pump 120Gbps real data center traffic
Start sending intrusion attacks through all the firewall ‘blades’
Demonstrate how 120Gbps of application traffic is load balanced among all the firewall ‘blades’
Demonstrate attacks being blocked under heavy data center application traffic
See the resiliency and redundancy of the Dell SonicWALL 120Gbps of Intrusion Prevention and Application Identification in real time (Walking with us down the disaster lane)
Demonstrate resiliency by taking out 25% of the firewalls (4 out of 16) and 50% of the switches (2 out of 4) will have next to no effect on traffic

## Slide 81
Solution Architecture (Connectivity)
Demo Rack

## Slide 83
Solution Architecture deep dive (IXIA, real world traffic)
IXIA/BreakingPoint offers an all-in-one security and performance testing platform for massive-scale, Stateful layer 4-7 application and security testing.
IXIA IPS Core data center traffic Profile
6 X40G link used from IXIA
PerfectStorm Traffic Generator
Dell SonicWall firewall Application Identification dashboard

## Slide 84
Solution Architecture deep dive (IXIA, real world attacks)
IXIA/BreakingPoint generates real world security attacks
Dell SonicWall block all the security attacks

## Slide 85
Solution Architecture (walking down the disaster lane)
X
X
X
X
X
X

## Slide 86: Transform NGFW economics and Data Center agility
10GbE
Dell Networking S5000
SuperMassive 9800
Dell can deliver cost savings up to 85%* lower than Cisco, 57% lower than Palo Alto Networks and up to 53%* lower than Fortinet
Competitor Deployment
Dell FireWALL Sandwich
The price of the Cisco ASA CX SSP-60
Better price per Protected Mbps than the Palo Alto Networks
5060
Higher IPS throughput than the Check Point
Higher IPS throughput than the Fortinet
Better scalability (connections/s) than Palo Alto Networks
1/2*
40%*
3X*
2X*
2X*
1+1 Active/Passive
Firewall layer
Switch layer - ingress
Switch layer - egress
Infrastructure utlilization
100%
* All pricing and performance figures taken from published information for comparable model or configurations.
Dell Networking S5000
N+1 Active
Firewall layer
10GbE

## Slide 87: Roadmap for Force 10 and SM integration

## Slide 88: VLT Sandwich
What is VLT? Virtual Link Trunking
  Layer 2 multipathing,
  creating redundancy through increased bandwidth (LACP)
  enabling multiple parallel paths between nodes and load-balancing traffic where alternative paths exist
  VLTi – for heartbeat status of VLT peer
  Faster convergence, Better resiliency
  VLT peers can be independently maintained
    (Reboots, FOS upgrades etc)
VLT Domain 1
VLT Domain 2

## Slide 89: Competitor Layer 2 Multipath designs (non VSS)

## Slide 90: Competitive designs– Juniper MLAG

## Slide 91: Active-Active MC-LAG

## Slide 92: Cisco vPC with ASA-X
Ether Channel can have only 8 active interfaces out of 16 maximum

## Slide 93: Contrasting deployment capabilities Transparent mode vs Dell Wire mode
Juniper SRX
  Rarely deployed in transparent mode
  No Support for VPN or NAT in transparent mode
    Support all UTM services
  Has a command called Packet mode: disables session tracking
    does not support stateful, L7 app firewalls, and UTM
Cisco ASA-X
  Very similar to our Layer 2 bridge mode
  Must have IP address assigned (bridge not wire)
  Passes most Layer 2-3 type traffic
  Support IPS and Next gen functions
  No QOS or DHCP Relay Support
  Unsure about disabling stateful or session tracking

## Slide 94: Firewall Sandwich and AAC as Configuration Synx

## Slide 95: Firewall Sandwich and AAC
Using the strength of Sandwhich with the Strenght of our HA protocols
AAC Purely used as Configuration Sync
Cluster Link 1
Cluster Link 2
Cluster Link 2
Cluster Link 1

## Slide 96: Firewall Sandwich and AAC - benefits
Single Configuration
Synchronized Firmware Upgrade
Cluster Link 1
Cluster Link 2
Cluster Link 2
Cluster Link 1

## Slide 97: Firewall Sandwich and AAC - Caveats
WireMode in AAC not officially supported
WireMode in AAC needs to be turned on in Diag page
Limit of 4 Nodes
Cluster Link 1
Cluster Link 2
Cluster Link 2
Cluster Link 1

## Slide 98: What about compared to Active-Active Clusters

## Slide 99: Cisco’s A-A Cluster limitations
Unsupported Features
Unified Communications
Remote access VPN (SSL VPN and IPsec VPN)
The following application inspections:
– CTIQBE
– GTP
– H323, H225, and RAS
– IPsec passthrough
– MGCP
– MMP
– RTSP
– SIP
– SCCP (Skinny)
– WAAS
– WCCP
Botnet Traffic Filter
Auto Update Server
DHCP client, server, relay, and proxy
VPN load balancing
Failover
ASA CX module
Features applied to Individual units (not as a cluster)
QoS policy.
Threat detection
Resource management
IPS module
NAT Limitations
No Proxy ARP
No Interface PAT on individual interfaces
No roud-robin PAT pool
No static PAT for the following inspections
FTP
PPTP
RSH
SQLNET
TFTP
XDMCP
All Voice-over-IP applications

## Slide 100: Juniper A-A Cluster Limitations
Rarely deployed, Active-Passive is mostly utilized (per Junos cookbook author)
no state regarding UTM is synchronized between the cluster nodes. Stateful objects like UTM sessions will not be synchronized
Stateful active/active cluster mode is not supported.
Sophos antivirus scanning is not supported as part of the active/active chassis cluster implementation.
However they do support:
Content filtering, URL (Web) filtering, Antispam filtering, Express antivirus scanning, Full file-based antivirus scanning

## Slide 101: Resources and reference

## Slide 102: FWS Resources
People
  Daniel Cole, Product Line Manager – Enterprise Products
  Khanh Dang, Product Marketing Manager
  Mallik Vatti, Sr. Technical Engineer – SuperMassive Escalation Team
Stuff
  This document
  FWS white paper (draft)
  MoAPC (sizing)
  Switch and FW configs

## Slide 103: Dell SonicWALL with Dell Networking – extreme horizontal scalability with proven reference architectures
S5000
S5000
S5000
S5000
SM 9XXX
SM 9XXX
SM 9XXX
SM 9XXX
Flow-A ->
Flow-A ->
Flow-B ->
Flow-B ->
Flow-C ->
Flow-C ->
Flow-D ->
Flow-D ->
Ingress Layer
Egress Layer
Virtual Link Trunk (VLT)
Primary Port-Channel
Bypass Port-Channel
Optional
Very Dense Solution (Only 6-8 RU)
Lower Power Consumption
40 Gig Networking with 40 Gig Firewall

## Slide 104: Reference
http://www.slideshare.net/CiscoSecurity/firewall-deployment-2012-san-diego
http://www.proteus.net/community/blogs/srx-flow-processing-and-ha-clustering
http://junos.com/techpubs/en_US/junos12.1x45/topics/concept/utm-chassis-cluster-overview.html
http://www.cisco.com/c/en/us/td/docs/security/asa/asa90/configuration/guide/asa_90_cli_config/intro_fw.html#29350
http://www.cisco.com/c/en/us/support/docs/security/pix-500-series-security-appliances/97853-Transparent-firewall.html#unsupp
http://howdoesinternetwork.com/2012/transparent-firewalls